## Slide 1: Q3 2026 Plant Performance Review
Atlas Precision Components | Dayton, Monterrey, Brno
Reporting period: 1 July to 30 September 2026
Prepared by Operations Excellence for the Executive Operations Committee
Synthetic data for a software demonstration; all companies, plants and people are fictional
Notes: Title slide.

## Slide 2: Executive summary
Plan attainment was 98.6 percent across the three plants: 399,311 good units against a target of 404,800 (12 weeks, 6 July to 27 September).
Scrap rate was 1.35 percent of units started on work orders completed in the quarter. Monterrey was above its 1.2 percent target at 1.46 percent; Dayton and Brno met theirs.
25 unplanned failures cost 536.5 hours of downtime. Dayton (237.8 h) and Monterrey (185.2 h) missed their downtime targets; Brno (113.5 h) met its target.
Spindle bearing wear (SPN-BRG) caused 53 percent of unplanned downtime hours.
Quality escape: 8D-2026-014, bore oversize on valve body AP-3312 from CNC lathe MTY-LTH-04 at Monterrey, $12,845 of nonconforming parts; closed 18 September.
Atlas Precision Components | Q3 2026 Plant Performance Review | Synthetic data | 2
Notes: Figures in this deck are computed from the plant operations tables as of 30 September 2026.

## Slide 3: Plant scorecard
Plant | Plan attainment | Scrap rate | Unplanned failures | Unplanned downtime | Defect cost
Dayton Plant | 99.8% | 1.20% (target 1.4%) | 12 | 237.8 h (target 210 h) | $34,955
Monterrey Plant | 95.8% | 1.46% (target 1.2%) | 8 | 185.2 h (target 160 h) | $34,152
Brno Plant | 100.8% | 1.41% (target 1.6%) | 5 | 113.5 h (target 140 h) | $21,612
All plants | 98.6% | 1.35% | 25 | 536.5 h | $90,719
Plan attainment is the sum of actual units divided by the sum of target units in the weekly output plan, for the 12 weeks starting 6 July to 21 September 2026.
Scrap rate is scrapped units divided by units started, for work orders completed from 1 July to 30 September 2026.
Unplanned downtime is the sum of downtime hours of unplanned maintenance events started in the quarter.
Atlas Precision Components | Q3 2026 Plant Performance Review | Synthetic data | 3
Notes: Targets come from the production plan workbook, scrap_targets sheet.

## Slide 4: Unplanned downtime by plant and month
Chart: Unplanned downtime (hours)
| July | August | September
Dayton Plant | 24.9 | 54 | 158.9
Monterrey Plant | 92.3 | 66 | 26.9
Brno Plant | 17.3 | 11.4 | 84.8
Dayton had the most unplanned downtime in the quarter: 12 events, 237.8 hours.
Monterrey's longest outage of the quarter was SPN-BRG on MTY-LTH-04 on 24 August (52.0 hours).
Brno stayed under its target of 140 hours.
Atlas Precision Components | Q3 2026 Plant Performance Review | Synthetic data | 4
Notes: Monthly unplanned downtime hours, summed by plant.

## Slide 5: Quality: where the cost came from
Defect type | Records | Pieces affected | Cost (USD)
dimension_oob | 48 | 1,054 | 41,860
burr | 21 | 417 | 15,990
crack | 13 | 210 | 11,683
surface_finish | 24 | 357 | 7,569
thread_defect | 8 | 161 | 7,306
144 defect records were logged in Q3 with a total cost of $90,719.
Monterrey carried $34,152 of that cost, of which $12,845 was the bore-diameter defects on AP-3312 (8D-2026-014).
Root cause: spindle bearing wear on MTY-LTH-04 with PM-2 running late; corrective actions closed on 18 September.
Atlas Precision Components | Q3 2026 Plant Performance Review | Synthetic data | 5
Notes: Defect cost is scrap value plus rework cost; use-as-is and return-to-supplier records carry no cost.

## Slide 6: Reliability: top failure codes in Q3
Failure code | Failure | Events | Downtime hours
SPN-BRG | Spindle bearing wear | 6 | 285.5
PMP-WEAR | Hydraulic pump wear | 2 | 85.7
SRV-DRV | Servo drive fault | 5 | 56.7
COOL-PMP | Coolant pump failure | 6 | 50.5
VLV-STK | Valve sticking | 2 | 22.0
The top two codes, SPN-BRG and PMP-WEAR, account for 69 percent of unplanned downtime hours.
54 PM-2 services were completed in the quarter (21 at Dayton, 18 at Monterrey, 15 at Brno).
Atlas Precision Components | Q3 2026 Plant Performance Review | Synthetic data | 6
Notes: Failure codes are defined in PM-MAN-001, Table 3.

## Slide 7: Supplier quality
19 material_flaw defects were logged in Q3, 258 pieces; 15 records were returned to the supplier.
The Halvorsen Alloys agreement (SQA-HAL-2026) targets 500 PPM and a lot rejection rate of at most 1.0 percent.
Supplier recovery plans are required if PPM is above twice the target in any quarter.
Atlas Precision Components | Q3 2026 Plant Performance Review | Synthetic data | 7
Notes: The supplier quality agreement is version 2.1, effective 1 January 2026.

## Slide 8: Priorities for Q4
Keep every PM-2 inside the interval in PM-MAN-001, Table 1; the CMMS blocks new work orders on machines more than 14 days past due.
Route vibration and temperature warnings to named owners at every plant.
Review gauge plans for valve body parts after 8D-2026-014.
Close the Dayton downtime gap: its largest cause in Q3 was spindle bearing wear (SPN-BRG, 101.5 hours).
Atlas Precision Components | Q3 2026 Plant Performance Review | Synthetic data | 8
Notes: Owners and dates are tracked in the Q4 operations plan.